## Slide 1
Project Status
Review #2
AMSAT
FOX-PLUS
ENGINEERING
March 5, 2025
FOX-PLUS
Notes: FOR OFFICAL USE ONLY

## Slide 2
FOX-Plus Project Status Review #2
Purpose and Overview
- System Overview
II. Mechanical
- Structure
III. Hardware
- Printed Circuit Boards (PCB) Status
IV. Software
- Software Development
- Software Testing
V. Integration & Testing
- Interconnections
VI. Summary and Next Steps
2
FOX-PLUS

## Slide 3
FOX-Plus Project Status Review #2
Purpose of this PSR
The purpose of this PSR is to determine the readiness of the Fox-Plus project for Preliminary Design Review.
AMSAT PDR has 3 Main Purposes:
Evaluation of initial state of the design against the proposed system/subsystem
requirements (“desirements”)
2. Provide a common “status state vector” for all developers, operators, et al, specifically:
- Cross team communication
- Opportunity for design teams to explain their design approach and present the status of
each subsystem
- Identify major problem areas/risks/obstacles and planned migration actions under the EM
phase
3. Provide a record of design decisions and the motivating reasons
3
FOX-PLUS

## Slide 4
FOX-Plus Project Status Review
Overview: Fox-Plus Presentations
Project Status Update - October 25, 2024
Project Status Review #1 – November 6, 2024
Project Status Review #2 – March 5, 2025 will show the progress made since the last PSR and will concentrate on the system integration of the components
4
FOX-PLUS

## Slide 5
FOX-Plus Project Status Review
Overview: Core Fox-Plus Engineering Team
Andrew Robinson, KA3WDW – Mechanical Engineer
Burns Fisher, WB1FJ – Software Lead
Will Brozovic - Software Engineer
Cliff Jenkins, KE8JAE – Software Engineer
Patrick Thomas, KB8DGD – Embedded Software, ICD
Mike Moore, K4MVM – System Engineer, Integration
Dave Hartrum, WA3YDZ – ICR v2.2
Leandra MacLennan, AF1R - Hardware Engineer, BOB
5
FOX-PLUS

## Slide 6
FOX-Plus Project Status Review
Overview: Changes & Updates Since PSR #1
Decision to use adapter card for ISIS to AMSAT board integration vice “one size fits all” LIHU – revert to LIHU v6
Progress in software and integration efforts to be presented here
Antenna deployment (ISIS Antenna System integration) successfully tested
ISIS to AMSAT interface signals and connectors identified
6
FOX-PLUS

## Slide 7
FOX-Plus Project Status Review
Overview: Documentation
LTM Interface Control Document (ICD):
  Version 2.0 draft started in late Q3 2024 to improve:
    Editorial Changes
      Typos, references to “university partner” etc.
    Appendix to separate “LTM” and Fox+ integration topics
    Updates to I2C, CAN, UART messages/support
    Add updated pinout and mechanical specifications
  Placed on hold in Nov 2024 due to adapter board decision which impacted board dimensions and changed signals from PC-104 connector to QxH
  Status: Awaiting further information regarding the updated design.
7
FOX-PLUS

## Slide 8
FOX-Plus Project Status Review
8
FOX-PLUS
Fox-Plus System Overview

## Slide 9
FOX-Plus Project Status Review - Structure
9
FOX-PLUS
ISISpace AntS
ISISpace Power Battery Pack (PBP)
Adapters
RXTX
ICR
LIHU
ISISpace Power Integration Unit (PIU)
ISISpace 1U Frame
TBD Payload
Adapters
SA’s not shown...obviously

## Slide 11
FOX-Plus Project Status Review - Structure
11
FOX-PLUS
Things To Do (on the road to CDR):
Clean up ISISpace-to-FOX-ME-113 adapter concept
Determine mounting schema – fasteners, threaded rods, keenserts
Perform tolerance stack up – determine tolerancing needs for new parts and potential shimming
Select hardware – material, type, finish, grade
Lay out cable paths
Develop assembly procedures – leverage Autodesk Inventor to lay out steps to put assembly together
Mature MEL / mass properties
Perform analysis – structural, thermal, etc.
Build GD&T drawings for fabricated parts
Snap a baseline in Git-Hub – review and approve design (model and/or drawings) and push to main trunk
Weird blue lines are in the provided SA models

## Slide 12
FOX-Plus Project Status Review
Structure
Adapter(s) for AMSAT boards into frame Options
Andrew is looking into
Adapters top and bottom of stack as shown in slide 8
Fasteners going different directions (as per Dave’s suggestion at S&S)
- may run into access issues for bolt tightening
Use cabling vice board for electrical
Use hybrid of pcb and cable for electrical
12
FOX-PLUS

## Slide 13
FOX-Plus Project Status Review
Hardware: PCB Status
- Improved Command Receiver (ICR) V2.2
PSR #1 Status: ICR design has been updated as follows:
- LNA device change from MICRF3000(now EoL) to MAX2634
- Changed TCXO powering back to earlier version when it was switched based on RX_ENABLE signal. This is a significant power consumption reduction.
- RSSI comparator device changed to a true comparator, not an op-amp
- Baseband audio filter now uses 3 op-amp stages. Response optimized.
- Component layout around SA636 device changed to optimize performance.
- Fudicials added to the PWB to facilitate Contract Manufacturer assembly.
13
FOX-PLUS

## Slide 14
FOX-Plus Project Status Review
Hardware: PCB Status - ICR V2.2
ICR v2.2 current status:
One ICR v2.2 board has been fully assembled and 90% tested
- SPI bus connections and A/D functionality not tested yet
Signal connections verified
Design changes to the LNA, SA636 layout, RSSI comparator and baseband audio
filter are fully tested and performing as expected
Two issues have been found that will require another PCB spin:
- Baseband audio signal trace to modem chip is shorted to ground by misplaced
vias
- Device footprint error on D2 causing missing connection
Some other minor tweaks to the design are BoM changes
PCB design update via KiCad should be completed by this weekend so new boards
can be ordered
Plan to assemble and white wire fix a second EM board so there will be 2 EM
boards that could support early S/C EM testing.
14
FOX-PLUS

## Slide 15
FOX-Plus Project Status Review
Hardware: PCB Status
- RXTX board
Previous Status: the RXTX board is being worked by Eric.
This work is in progress
Works well on ME-SAT!
Current Status: Dan Habecker building boards.
15
FOX-PLUS

## Slide 16
FOX-Plus Project Status Review
Fox-Plus PCB Versions and Status
16
FOX-PLUS
PCB | Current Version | Fox-Plus-A Version | Status | Responsible Engineer
LIHU | v1.1 | v6 (1.3?) | New boards in approx. 2 wks | Bdale Garbee
ICR | V1.2 | v2.2 | In build / testing | Dave Hartrum
RX/TX | V1.1 | v2.1 | Parts needed for build | Dan Habecker

## Slide 17
FOX-Plus Project Status Review
Software Development
PSR#1 Status: Will Brozovic and Cliff Jenkins have each setup development tools and have attended training sessions with Burns
Will has IDE Linux machine both working. He can compile and upload the flight software to the IHU he has. Computer runs Ubuntu Linux and he interfaces to the IHU with an STLink.
Cliff has worked on the repositories and has them ready for Fox+ development. He has IDE and Linux machine set up, can compile and upload flight software to the IHU he has onhand. He is currently testing the STLink.
Current Status: both developers are working on aspects of Fox-Plus software development. One area is to trim out unneeded GOLF code.
17
FOX-PLUS

## Slide 18
FOX-Plus Project Status Review
Software:
- AMCOM Over-The-Air (OTA) Software
Software application that runs on MS Windows
This software does not need significant changes. A text file defines each satellite including commands and codes available for it. Heimir can make changes for F+ IHU if needed
18
FOX-PLUS

## Slide 19
FOX-Plus Project Status Review
Software:
- Fox Telecom – Ground Station Software
This software does not need significant changes and can be done in the future
19
FOX-PLUS

## Slide 20
FOX-Plus Project Status Review
Software: Testing
Flight Software: HuskySat flight software used for basic tests and antenna deployment with little modification
- successful testing, including antenna deployment but needs cleanup
AMCOM OTA software modified from HuskySat tested successfully
Telemetry, ground station GUI (Fox-in-a Box) not tested in detail
- verified frames being received, modes indicated properly
20
FOX-PLUS

## Slide 21
FOX-Plus Project Status Review
Software: Testing (firmware)
USB Loader - pyMicroloader
Worked with Burns to get pyMicroloader running on my Ubuntu 24.04 test bench PC
- initial problems due to elftools module incompatibility with Ubuntu version or other module. Used Bill Schell’s python tools versions to get it working.
Necessary for me to be able to load flight software versions as I’m the only one with HuskySat LIHU which is necessary for ISIS AntS testing
21
FOX-PLUS

## Slide 22
FOX-Plus Project Status Review – Integration & Testing
22
FOX-PLUS
Fox-in-a-Box
Power Supply
AntS
EGSE
PIU
LTM
Logic Analyzer
PC

## Slide 23
FOX-Plus Project Status Review
System Integration & Testing – ISISpace EPS Components
Electrical Ground Support Equipment (EGSE) module
- The EGSE is used to switch between bench power supply and batteries to the ISIS Power Integrated Unit (PIU)
PSR#1 Status: this unit has not been interconnected to the Fox-Plus IHU as yet. It cannot be connected to the LIHU due to pins being used contrary to the CSKB “standard”. The I2C software interface has not been tested as it is not yet available
23
FOX-PLUS

## Slide 24
FOX-Plus Project Status Review
System Integration & Testing – ISISpace EPS Components
Electrical Ground Support Equipment (EGSE) module
- The EGSE is used to switch between bench power supply and batteries to the ISIS Power Integrated Unit (PIU)
Current Status:
Power to PIU tested using bench power supply
ISIS battery pack charged using bench PS and EGSE
Power to the LTM from the PIU successfully tested using CSKB light (PC104) 5v regulated for v-sys on Feb 3, 2025
24
FOX-PLUS

## Slide 25
FOX-Plus Project Status Review
System Integration & Testing
LIHU to ISIS Antenna System (AntS)
PSR#1 Status: We have two AntS. I have one, Andrew has one. I have tested antenna deployment with AMCOM Over the Air (OTA) commands – had minor problem, needed override. Interconnect cable uses expensive Omnetics connectors / cable (more in Fox+ IHU slide)
25
FOX-PLUS

## Slide 26
FOX-Plus Project Status Review
System Integration & Testing
LIHU to ISIS Antenna System (AntS)
Current Status:
No change in AntS locations
Omnetics onboard and cable connectors A29100-009, A28000-009 very expensive; replaced with Harwin connectors
- onboard connector to be located on adapter card
- current testing achieved with Omnetics connectors
Software commands for antenna deployment tested and working correctly
Burn wire restring accomplished – ordering more burn wires
FOX-PLUS
26

## Slide 27
FOX-Plus Project Status Review
System Integration & Testing: Omnetics connector on LIHU
4
FOX-PLUS

## Slide 28
FOX-Plus Project Status Review
System Integration & Testing: Omnetics to Harwin Test Cable
28
FOX-PLUS

## Slide 29
FOX-Plus Project Status Review
System Integration & Testing: Antennas Deployed
29
FOX-PLUS

## Slide 30
FOX-Plus Project Status Review
System Integration & Testing: Antennas Restrung & Burn Wires
30
FOX-PLUS

## Slide 31
FOX-Plus Project Status Review
System Integration & Testing: Preliminary Adapter
LIHU to EPS Adapter
31
FOX-PLUS

## Slide 32
FOX-Plus Project Status Review
System Integration & Testing: Adapter Connector Interfaces
> H1, H2: These two 52 pin connectors make up the PC104 and the CubeSat Kit Bus (CSKB) light pin designations
> QSH (J3): Stacking Connector, Fox bus
J4: AntS interface connector
Two I2C busses and One CAN bus are used, also a UART interface
Other connectors / interfaces needed, not yet developed:
1. Umbilical connectors
2. Solar Panel connectors
32
FOX-PLUS

## Slide 33
FOX-Plus Project Status Review
System Integration: ISISPACE Solar Panels
Previous Status: Zach is shipping the 10 ISISPACE Solar Panels to me. I will keep 5 and ship 5 to Andrew for EM build.
Current Status: Andrew and I each have one set of solar panels
The solar panels require interface wires to be soldered for integration into the assembled cubesat. Instructions (User’s Manual) have been provided by ISISpace. This has yet to be done.
33
FOX-PLUS

## Slide 34
FOX-Plus Project Status Review
Summary: Known Unknowns
Umbilical connector, scheme to charge the batteries and interface UART once the Fox-Plus-A is fully assembled and in dispenser
Solar panel wiring / routing not designed
34
FOX-PLUS

## Slide 35
FOX-Plus Project Status Review
V. Summary: Next Steps
Determine and produce the adapter(s) to accommodate AMSAT boards in the ISIS frame
Design and build adapter card to interface the LIHU v6 to the ISIS EPS and AntS
Software: command and response to / from ISIS EPS
Need to get Break Out Boards and LIHUs to Cliff, Patrick, Chris
35
FOX-PLUS

## Slide 36
2022
ConOps
Complete
11 Feb 22
SRS
Complete
07 Dec 22
2023
2024
Target
PDR
Jun 24
PSR #2
High Level System Design:
COTS Components (ISISPACE)
Begin Rcv ISISpace Components Jan 24
Eval & Test ISISpace Components
Rcv Solar Panels
21 Oct 2024
Fox-Plus-A
High Level Schedule
202
Ready for
Launch
Q1
Target CDR
Sep/Oct 25
2025
2026
36