Date:
Version: Version 0.2
# Fox-Plus

# System Requirements Specification
# Introduction
### IF YOU CAN SEE THIS TEXT PLEASE TURN OFF “DISPLAY HIDDEN TEXT” IN YOUR MICROSOFT WORD. THIS HIDDEN TEXT IS USED FOR REQUIREMENTS TRACKING.
This document specifies the system level requirements for the first satellite of the AMSAT Fox-Plus satellite project. The initial Fox-Plus satellite will be a 1U CubeSat with later Fox-plus satellite increasing in size and capability.

The Fox-Plus project is intended as a follow-on and upgrade to the initial Fox-1 series CubeSat satellites. The first four Fox-1 satellites flew single channel FM repeaters as their bus-supporting communications system. The fifth and final Fox-1 satellite RadFxSat-2, had essentially the same configuration and basic bus structure as the earlier Fox-1 satellites, but with their single channel FM repeater transmitter and receiver replaced with a new wideband linear transponder (LT) This type of amateur radio communications system will provide more channels for multiple, simultaneous radio contacts, as well as a higher data rate, continuous telemetry downlink.

In addition to its mission as a communications satellite, Fox-Plus will host an experiment payload. The satellite will reserve mass and volume for the experiment and will provide DC power and communications capability to support experiment data downlinking.

## Document History
DATE	VERSION	AUTHOR	SUMMARY
May 12, 2022	V0.1	M. Moore (K4MVM)	Initial draft
	V0.2	J. Brandenburg (KF5IDY)	Overall content revision

## Document Scope
The purpose of this document is to specify the requirements of the satellite at the system (i.e., "black box") level. It is intended to be used by hardware, software and mechanical designers to develop architecture/high-level design specifications. It is also intended to be used for test planning and development.

## Document Format
This document provides requirements in numbered format. Each requirement is assigned a unique number. Additional information such as comments or examples provided for guidance or clarity is italicized to distinguish it from specific requirements.

## References
1. AMSAT Fox-Plus Concept of Operations, Version 1.1, August 16, 2022
2. CubeSat Design Specification, Rev. 14.1, February 2022, The CubeSat Program Cal Poly SLO.
3. Launch Services Program, Program Level Dispenser and CubeSat Requirements Document, LSP-REQ-317.01 Revision B, January 30, 2014, National Aeronautics and Space Administration (NASA).
4. Spaceflight, Inc. General Payload Users Guide SF‐2100‐PUG‐00001, Rev F 2015‐22‐15, May 22, 2015.
5. ITU Radio Regulations, Edition of 2020, available from https://www.itu.int/pub/R-REG-RR.
# General Requirements
## CubeSat Requirements
### FOX1:SR:2.1.1 The satellite shall satisfy the requirements specified in Spaceflight, Inc. General Payload Users Guide SF‐2100‐PUG‐00001, Rev F 2015‐22‐15, May 22, 2015.
### The satellite shall satisfy the requirements specified in the CubeSat Design Specification, Rev. 14.1. [FOX1:CR:1][FOX1:CR:35]{Implementor = MECH}~
### FOX1:SR:2.1.2 The satellite shall satisfy the requirements specified in the NASA LSP-REQ-317.01 Revision B. [FOX1:CR:1][FOX1:CR:37] {Implementor = MECH}~
### FOX1:SR:2.1.2 The satellite shall satisfy the debris and deorbit requirements specified in FCC regulations as documented in Title 47 Section 5.64 https://www.ecfr.gov/current/title-47/section-5.64.
### FOX1:SR:2.1.3 The satellite shall satisfy the requirements for a 1 Unit (single) CubeSat.[FOX1:CR:1][FOX1:CR:35] {Implementor = MECH}~
### FOX1:SR:2.1.4 The satellite shall provide mass for an experiment payload up to 100 g.
### The satellite shall provide volume for an experiment payload up to 92 x 92 x 31.4 mm. [FOX1:CR:7] {Implementor = MECH;EXP}~
## FOX1:SR:2.1.5Environmental Requirements
### FOX1:SR:2.2.1 The satellite avionics shall be designed for an operating temperature range of -400C to +850C.[FOX1:CR:1][FOX1:CR:35][FOX1:CR:37] {Implementor = MECH;RFTX;RFRX;IHU;PSU;BATT;EXP;ANT}~
### FOX1:SR:2.2.2 The satellite shall be designed to operate in an approximate 500 to 700 kmy, circular orbit. [FOX1:CR:2] {Implementor = MECH}~
### FOX1:SR:2.2.3 The satellite shall be designed to tolerate the radiation environment in orbit.[FOX1:CR:2] {Implementor = MECH;RFTX;RFRX;IHU;PSU;BATT;EXP;ANT}~
## Reliability Requirements
### FOX1:SR:2.3.1 The satellite shall be designed for a minimum 5-year, on-orbit lifetime. [FOX1:CR:19] {Implementor = MECH;RFTX;RFRX;IHU;PSU;BATT;EXP;ANT}~
## Radio Frequency (RF) Regulatory Requirements
### FOX1:SR:2.4.1 The satellite’s RF transmitter shall meet or exceed the requirements specified in ITU Radio Regulations, Volume 1 Articles, Chapter 1 – Terminology and Technical Characteristics of Stations, Article 3.[FOX1:CR:36] {Implementor = RFTX}~
### FOX1:SR:2.4.2 All satellite uplinks shall be in the 2 meter band of the Amateur Satellite Service. [FOX1:CR:5] {Implementor = RFRX}~
### FOX1:SR:2.4.3 All satellite downlinks shall be in the 70 cm band of the Amateur Satellite Service. [FOX1:CR:6] {Implementor = RFTX}~
### FOX1:SR:2.4.4 All satellite transmitter and receiver generated frequencies shall deviate by no more than 5 parts-per-million from their specified values including initial accuracy and temperature variation.[FOX1:CR:36] {Implementor = RFTX}~
### FOX1:SR:2.4.5 All satellite frequencies shall be coordinated with the IARU.[FOX1:CR:21] {Implementor = RFTX;RFRX}~

### The command uplink shall be a narrow band FM signal (+/- 5 kHz deviation) located outside of the user transponder passband.[FOX1:CR:21] {Implementor = RFTX;RFRX}~
The band plan with the actual coordinated frequencies will be specified in a separate document.
# Functional Requirements
## Antenna System
### FOX1:SR:3.1.1 The satellite shall include a deployable antenna system. [FOX1:CR:9] {Implementor = ANT}~
## Attitude Control
### FOX1:SR:3.2.1 The satellite shall incorporate passive magnetic stabilization to align the deployed antennas with the magnetic field of the earth. [FOX1:CR:8] {Implementor = MECH}~
## Access Ports
### FOX1:SR:3.3.1 The satellite shall include a "Remove Before Flight" (RBF) pin as per the CubeSat Design Specification. [FOX1:CR:22] {Implementor = MECH;PSU;BATT}~
### FOX1:SR:3.3.2 The satellite shall include an umbilical port as per the CubeSat Design Specification. [FOX1:CR:23] {Implementor = MECH;IHU}~
## Pre-launch Features
### FOX1:SR:3.4.1 The satellite battery and photovoltaic panels shall be electronically disconnected from the avionics when the "Remove Before Flight" pin is inserted, regardless of the state of the deployment switch(es). [FOX1:CR:22] {Implementor = MECH;PSU;BATT}~
### FOX1:SR:3.4.2 The satellite shall provide a means to charge the battery via the umbilical port while integrated with the dispenser. [FOX1:CR:11] [FOX1:CR:23] {Implementor = MECH;PSU;BATT}~
### FOX1:SR:3.4.3 The satellite shall provide a means to run diagnostic tests via the umbilical port while integrated with the dispenser. [FOX1:CR:23] {Implementor = MECH;IHU}~
## Power
### FOX1:SR:3.5.1 The satellite shall produce electrical power from sunlight. [FOX1:CR:10] {Implementor = MECH;PSU}~
### FOX1:SR:3.5.2 The satellite shall produce electrical power while in sunlight regardless of orientation and while tumbling or spinning. [FOX1:CR:10] {Implementor = MECH;PSU}~
### FOX1:SR:3.5.3 The satellite shall produce sufficient average electrical power to operate continuously in the orbit of maximum eclipse. [FOX1:CR:11] {Implementor = PSU;BATT}~
### FOX1:SR:3.5.4 The satellite shall provide sufficient battery capacity to operate continuously in the orbit of maximum eclipse. [FOX1:CR:11] {Implementor = PSU;BATT}~
### The satellite shall not provide battery power to the main bus until approximately 115 seconds after activation of both deployment switches indicating successful launch vehicle dispenser separation.

## Experiment
### FOX1:SR:3.6.1 The satellite shall provide DC power for an experiment payload. [FOX1:CR:7] [FOX1:CR:31] {Implementor = PSU;EXP}~
### FOX1:SR:3.6.2 The satellite shall provide a means to activate and deactivate the experiment payload. [FOX1:CR:7] {Implementor = IHU;EXP}~
### FOX1:SR:3.6.3 The satellite shall provide a means to telemeter data from the experiment payload. [FOX1:CR:7] [FOX1:CR:16] {Implementor = IHU;EXP}~
The experiment payload details will be specified in a separate document.

## RF Uplink
### FOX1:SR:3.7.1 The satellite shall include a linear uplink receiver. [FOX1:CR:3] {Implementor = RFRX}~
### FOX1:SR:3.7.2The uplink receiver shall process signals in a linear manner. The receiver will process SSB, CW, PSK, and FSK signals to its intermediate frequency with intermodulation distortion (IMD) products no higher than -50 dBc when the maximum intended level signals are applied to the spacecraft. [FOX1:CR:21] {Implementor = RFRX}~
## RF Downlink
### FOX1:SR:3.8.1The satellite shall include a linear downlink transmitter. [FOX1:CR:3] {Implementor = RFTX}~
### FOX1:SR:3.8.2The downlink transmitter shall be a linear transmitter with intermodulation products no higher than -20 dBc when the highest level output signal is at maximum output power. [FOX1:CR:4][FOX1:CR:21] {Implementor = RFTX}~
## Transponder
### FOX1:SR:3.9.1 The satellite shall provide linear transponder operation via the RF uplink and RF downlink. [FOX1:CR:3] [FOX1:CR:25] {Implementor = RFTX;RFRX}~
### FOX1:SR:3.9.2 The user transponder shall have a -3dB bandwidth of 30 kHz and a -20dB bandwidth of 50 kHz, referenced to the center of the passband. [FOX1:CR:21] {Implementor = RF}~
### FOX1:SR:3.9.3 The transponder shall be an inverting transponder. [FOX1:CR:21] {Implementor = IHU;RFTX}~

### The transponder shall have a means of sensing and adjusting gain so that the highest level throughput signal is not distorted with intermodulation products higher than -20 dBc with multiple signals in the passband.
### The transponder gain adjustment shall have a time constant of <TBD> seconds, so that the highest level signal in the passband will not ‘pump’ other signals in the passband by its modulation.[FOX1:CR:21] {Implementor = IHU;RFTX}~
### The transponder shall have a mechanism for detecting the level of signals in the uplink passband. This aggregate level shall have a threshold switching mechanism for deactivating the satellite transmitter when no signals exceed the threshold. The transmitter shall be activated when the threshold is exceeded for approximately one second. The threshold mechanism shall continue to keep the transmitter activated for 30 seconds after the threshold conditions are no longer satisfied.
### The transponder shall have a linear gain such that a received CW signal of <TBD> dBm will result in a power output of +20 dBm. Any other signals amplified in the passband shall create IMD products not to exceed -20 dBc in the passband of the transponder.

## Telemetry Data
### FOX1:SR:3.10.1 The satellite shall collect telemetry data. [FOX1:CR:15] {Implementor = RFTX;RFRX;IHU;PSU;BATT}~
### FOX1:SR:3.10.2 The telemetry data shall include at a minimum, the measured parameters shown in Table 1. [FOX1:CR:15] {Implementor = RFTX;RFRX;IHU;PSU;BATT}~

Table 1
PARAMETER NAME	DESCRIPTION
CELL V	Voltages of battery cells
PANEL V	Voltages of solar panels
TOTAL I	Total DC current out of power system
PA I	DC current into RF power amp
BATTERY T	Temperature of battery
PANEL T	Temperatures of solar panels
TX T	Temperature of RF transmitter card
RX T	Temperature of RF receiver card

### FOX1:SR:3.10.3 The measured parameters shall be sampled at least every 15 seconds. [FOX1:CR:15] {Implementor = RFTX;RFRX;IHU;PSU;BATT}~
### FOX1:SR:3.10.4 The minimum and maximum values of each of the measured parameters shall be saved in non-volatile memory. [FOX1:CR:15] {Implementor = IHU}~
### FOX1:SR:3.10.5 The telemetry data shall also include at a minimum, the calculated parameters shown in Table 2. [FOX1:CR:15] {Implementor = IHU;PSU}~

Table 2
PARAMETER NAME	DESCRIPTION
UP TIME	Total seconds since avionics power-up or the last Reset
SPIN	Satellite spin rate and direction

### FOX1:SR:3.10.6 A telemetry frame shall include the current measured values, the saved minimum and maximum values, and the current calculated values. [FOX1:CR:15] {Implementor = IHU}~
The detailed telemetry interface will be specified in a separate document.

## Telemetry Transmission
### FOX1:SR:3.11.1 The satellite shall send slow speed telemetry using BPSK on the RF downlink. [FOX1:CR:14] {Implementor = RFTX;IHU}~
### FOX1:SR:3.11.2 The downlink telemetry signal shall be a 1200 bps BPSK signal located outside the user transponder passband and shall be part of the frequency multiplexed downlink.[FOX1:CR:21] {Implementor = RFTX;RFRX}~ The telemetry signal’s peak power level shall be no greater than <TBD> dB below the maximum output power of the transponder.
### FOX1:SR:3.11.3 Telemetry data shall be transmitted simultaneously with user transponder signals, and shall cease to be transmitted when the user transponder threshold signal “hang time’ of 30 seconds has expired. [FOX1:CR:15] [FOX1:CR:16] [FOX1:CR:17] [FOX1:CR:25] {Implementor = RFTX;IHU}~
### FOX1:SR:3.11.4 The telemetry transmission shall include telemetry frames. [FOX1:CR:15] [FOX1:CR:16] [FOX1:CR:17] {Implementor = IHU}~
### FOX1:SR:3.11.5 The telemetry transmission shall also include experiment data. [FOX1:CR:16] [FOX1:CR:17] {Implementor = IHU}~
## Command Capability
### FOX1:SR:3.12.1 The satellite shall provide a means to process commands sent via the RF uplink from authorized ground control stations. [FOX1:CR:12] [FOX1:CR:18] {Implementor = RFTX;IHU}~
### FOX1:SR:3.12.2 The command receiver shall be on a frequency outside the transponder bandwidth. [FOX1:CR:13] [FOX1:CR:18] {Implementor = RFTX;RFRX}~
### A 1200 bps AFSK-FM via a NBFM channel demodulation capability shall be provided to the IHU for the purpose of transferring data and commands to the IHU. This AFSK-FM channel shall follow the FSK requirements of Bell 202 modems.
### The uplink command receiver shall be capable of receiving and demodulating AFSK-FM signals at 1200 bps with an input signal level of -120 dBm with a baseband Bit Error Rate (BER) of 1 x 10-4.
### [FOX1:CR:18]`The command uplink receiver will not be responsible for bit or byte synchronization, re-timing, or error correction.

### FOX1:SR:3.12.3 The following commands shall be provided, as shown in Table 3, below. [FOX1:CR:13] [FOX1:CR:18] {Implementor = RFTX;IHU;PSU}~

Table 3
Command	Operation
SAFE MODE	Enter Safe Mode
INHIBIT TX	Inhibit RF transmission
ENABLE TX	Enable RF transmission
IHU OFF	Power off IHU
IHU ON	Power on IHU
CLEAR	Clear stored telemetry
TRANSPONDER MODE	Enter Transponder Mode
ENABLE AUTO-SAFE	Enable Auto-Safe Mode
DISABLE AUTO-SAFE	Disable Auto-Safe Mode

### FOX1:SR:3.12.4 A SAFE MODE command shall cause the satellite to enter the Safe Mode. [FOX1:CR:18] {Implementor = RFTX;IHU}~
### FOX1:SR:3.12.5 An INHIBIT TX command shall disable the RF transmitter. [FOX1:CR:18] [FOX1:CR:30] {Implementor = RFTX}~
### FOX1:SR:3.12.6 An ENABLE TX command shall enable the RF transmitter. [FOX1:CR:18] [FOX1:CR:30] {Implementor = RFTX}~
### FOX1:SR:3.12.7 An IHU OFF command shall cause the IHU System to power off. [FOX1:CR:18] {Implementor = IHU;PSU}~
### FOX1:SR:3.12.8 An IHU ON command shall cause the IHU System to power on. [FOX1:CR:18] {Implementor = IHU;PSU}~
### FOX1:SR:3.12.9 A CLEAR command shall cause the satellite to clear the saved minimum and maximum telemetry parameter values. [FOX1:CR:18] {Implementor = IHU}~
### FOX1:SR:3.12.10 A TRANSPONDER MODE command shall cause the satellite to enter the Transponder Mode. [FOX1:CR:18] {Implementor = RFTX;IHU}~
### FOX1:SR:3.12.11 An ENABLE AUTO-SAFE command shall enable the auto-safe mode state. [FOX1:CR:18] [FOX1:CR:34] {Implementor = RFTX;IHU}~
### FOX1:SR:3.12.12 A DISABLE AUTO-SAFE command shall disable the auto-safe mode state.
### FOX1:SR:3.12.13 The control interface details will be specified in a separate document.

## On-Orbit Operating Modes

### FOX1:SR:3.13.1The satellite shall provide on-orbit operating modes as shown in Table 4. [FOX1:CR:24] [FOX1:CR:25] [FOX1:CR:27] [FOX1:CR:34] {Implementor = RFTX;IHU}~

Table 4
NAME	DESCRIPTION
Startup Mode	Wait 50+ minutes and deploy antennas
Safe Mode	Wait 120 seconds then begin telemetry beacon sequencing; / Experiment powered off
Auto-Safe Mode	If enabled, automatically detects a low battery condition and shuts down some major satellite activities
Transponder Mode	Linear transponder mode; telemetry channel and experiment active

### The satellite shall transition between its on-orbit operational modes as shown in the State Transition Diagram in Figure 1. [FOX1:CR:24] [FOX1:CR:25] [FOX1:CR:27] [FOX1:CR:34] {Implementor = RFTX;IHU}~
### FOX1:SR:3.13.2
### FOX1:SR:3.13.3 Upon launch, a power cycle of the avionics, or after a reset action, the satellite shall enter the "START" point as shown in Figure 1. [FOX1:CR:33] {Implementor = IHU}~
### FOX1:SR:3.13.4 An IHU ON command shall also cause the satellite to begin operation from the "START" point as shown in Figure 1.[FOX1:CR:18] {Implementor = IHU}~
### FOX1:SR:3.13.5 If the antennas have not been deployed, the satellite shall enter Startup Mode. [FOX1:CR:9] [FOX1:CR:24] {Implementor = IHU}~
#### FOX1:SR:3.13.7 In Startup Mode, the satellite shall wait at least 50 minutes before commanding antenna deployment and initiating RF transmissions. [FOX1:CR:24] {Implementor = MECH;IHU;ANT}~
#### FOX1:SR:3.13.7.1 After the antennas have been successfully deployed upon initial orbit, the satellite shall enter Safe Mode.
### FOX1:SR:3.13.7.3 After a Reset action and antennas successfully deployed check, the satellite shall determine whether its last state was SAFE MODE.
#### FOX1:SR:3.13.5.1 If the last state was SAFE MODE, the satellite shall (re)enter SAFE MODE. [FOX1:CR:24] {Implementor = IHU}~
#### FOX1:SR:3.13.5.21200 bps BPSK telemetry beacon downlink channel operation shall occur during SAFE MODE[FOX1:CR:26] {Implementor = RFRX;IHU}~FOX1:SR:3.13.11. [FOX1:CR:26] {Implementor = RFRX;IHU}~ There shall be NO CW beacon functionality implemented in the satellite
#### If the last state was not SAFE MODE, the satellite shall enter TRANSPONDER MODE. [FOX1:CR:24] {Implementor = RFTX;IHU}~
#### In TRANSPONDER MODE, the transponder and the telemetry shall be active.FOX1:SR:3.13.6
### FOX1:SR:3.13.8 The command RF uplink shall be monitored for commands in all modes.
FOX1:SR:3.13.9
## Operational Timing Requirements
### FOX1:SR:3.13.1The satellite shall satisfy the operational times shown in Table 5. [FOX1:CR:24] [FOX1:CR:25] [FOX1:CR:27] [FOX1:CR:34] {Implementor = RFTX;IHU}~

Table 5
FUNCTION	TIME ( 5%)	OPERATIIONAL CONDITIONS
Burn Resistor Activation	 4 seconds	Time allotted for the (activated) burn resistors’ initial melting of the deployable antenna restrainers
Burn Resistors RE-activation	 20 seconds	Time allotted for the (RE-activated) burn resistors’ subsequent melting of the deployable antenna restrainers
Deployment Switch Notification Delay	 115 seconds	Delay time from deployment switch physical activation to electronic activation report.
IHU Boot-Up/POST	< 20 seconds	Time for the Internal Housekeeping Unit (IHU) to boot-up and run Power On System Tests (POST)
Antenna/RF Initiation Delay	 50 minutes	Antenna deployment and transmission inhibit time after dispenser launch
Beacon (Safe Mode) Duty Cycle	 2 minutes	Elapsed time from end of beacon telemetry transmission to start of next beacon transmission while in SAFE MODE
Hang Timer	 30 seconds	RF transmit carrier time after the uplink passband (aggregate) signal(s) no longer satisfy the threshold criteria.
Telemetry Period	 15 seconds	Sampling period for all telemetry parameters
ENABLE TX Confirm	 3 minutes	Time after receipt of ENABLE TX command before transmitting a telemetry beacon
Watchdog Timer	 10 seconds	If IHU-directed tasks do not report back within this time period, the satellite will reset.

# External Interface Documents
To fully specify the satellite’s technical requirements, the following documents should be consulted:
1. IARU Coordinated Frequency Plan
2. Downlink Specification
3. Control Interface Specification
4. Experiment Payload Specification

# Summary
The Fox-Plus satellite will be AMSAT's first linear transponder CubeSat. Its primary mission is to provide linear transponder communications capability. The secondary mission is to host a university-provided experiment payload.