## Slide 1: FoxPlus Mechanical Layout and Design
G. Andrew Robinson (gar3181@gmail.com)
KA3WDW
17Oct2025
43rd Annual AMSAT Space Symposium and Annual General Meeting
FoxPlus

## Slide 2
01 | FoxPlus Overview
02 | Hardware
03 | Integration Challenges
04 | SV Assembly
05 | Current Status
06 | Path Forward
Agenda

## Slide 3
FoxPlus Overview
1U CubeSat design leveraging heritage AMSAT electronic “guts”
Utilize COTS hardware to promote accelerated timeline to launch
  Hardware procured for FoxPlus-A and –B
LEO orbit

## Slide 4
FoxPlus COTS Hardware
Leveraging COTS 1U hardware from Innovative Solutions in Space (ISISpace) – isispace.nl
  1U Frame
  Power Battery Pack (PBP)
  Power Integration Unit (PIU)
  AntS UHF/VHF Deployable Antenna
  Solar Arrays (not shown)
Images from isispace.nl
1U Frame
AntS
Power Integration Unit
Power Battery Pack

## Slide 5
FoxPlus Layout Overview
ISISpace AntS
ISISpace Power Battery Pack (PBP)
FOX-ME-203 Mechanical Adapter
RXTX
ICR
LIHU
ISISpace Power Integration Unit (PIU)
ISISpace 1U Frame
FOX-ME-204 Power Signal Adapter (PSA)

## Slide 6
Integration Challenges
Non-symmetric ISISpace hole pattern (frame, PBP, and PIU) present an integration challenge with PCB’s built to FOX-ME-113
1U volume constraints restrict options to move the pattern in the XY-plane
Adapter design challenged by proximity of holes; thru-holes or keenserts needed to facilitate mountain schema
PCB stack-up considerations needed to maximize available space

## Slide 7
COA#1 – Adopt ISISpace Mounting
Pros | Cons
Easy mechanical integration | New boards need designed/made
Leverage ISISpace assembly | Incompatible design
Space efficient | New ICD

## Slide 8
COA#2 - Adapter Design
(8) M3 Helicoils
¾-X Section
(4) GOLF/FOX-ME-113 hole pattern on top (mate with RXTX/ICR/IHU stack)
(4) ISISpace hole pattern on bottom (mate with battery)
Minimal difference between hole patterns makes this challenging
Pros | Cons
Uses existing LTM design/boards | Complicated integration
 | Less space for PCBs
 | Shock/vibe risk

## Slide 9
Assembly Process

## Slide 10
Assembly Process

## Slide 11
Power Signal Adapter
GOLF/FOX-ME-113 Bolt Hole Pattern
Top
Samtec QSH-030-01-L-D-A
Bottom
92mm
96mm
(2) MTSW-106-08-L-D-300 -235
(2) MTSW-107-08-L-D-300 -235
PSA
PIU
LIHU

## Slide 12
Current Status
FOX-ME-204 Power Signal Adapter design finalized; release pending minor updates
FOX-ME-203 Mechanical Adapter drawing Work In Progress (WIP); metal parts fabricated and in-house
Hardware (fasteners, spacers, etc.) in-house; mechanical fit model constructed on ISISpace assembly jig
Solar Array “blanks” designed, fabricated, and in-house
FOX-ME-202 (TLA) and Assembly Procedures WIP

## Slide 13
Path Forward
Route wires/cables as needed leveraging built-in AutoDesk Inventor toolbox
Support Engineering Model (EM) buildup and subsequent tests
Finalize and release drawings and documents to support Flight Model build, test, and launch
Update design and layout as needed for FoxPlus-B

## Slide 14
End